## Slide 1
Inside the ADC
Every parameter on the datasheet, and what it actually costs you
Static · Dynamic · Timing · Bandwidth · Power
V_in
1 · Sample & hold
freeze V_in for one T_s
2 · Quantiser
nearest of 2ᴺ levels
3 · Encoder
level → N-bit code
N-bit
code
Clock f_s
every T_s = 1/f_s: hold → compare → output
Notes: This talk takes one component — the analog-to-digital converter — and walks through every number a datasheet quotes about it. Each parameter gets the same treatment: what it means in plain words, the equation, a picture, a real number, and what goes wrong when you ignore it.

## Slide 2
What an ADC does, in three steps
Opening
2
An ADC turns a voltage into a number. It does it in three steps, repeated on every tick of a clock: hold the voltage still, compare it against a ruler with 2ᴺ marks, and write down the mark number in binary.
Sample and hold: freeze the input so it cannot move mid-measurement
Quantise: decide which of the 2ᴺ levels the frozen voltage is nearest
Encode: output that level as an N-bit binary word
V_in
1 · Sample & hold
freeze V_in for one T_s
2 · Quantiser
nearest of 2ᴺ levels
3 · Encoder
level → N-bit code
N-bit
code
Clock f_s
every T_s = 1/f_s: hold → compare → output
≈
Think of it like this Measuring a child’s height: ask them to stand still, line them up against a marked ruler, write the number in the book. Repeat every birthday.
EXAMPLE
A 12-bit, 100 MSPS converter
4096 marks on the ruler, one reading every 10 ns
Output: 100 million 12-bit words per second = 1.2 Gbit/s
Every parameter in this talk describes how well one of those three steps is done
Notes: Frame the whole talk: static parameters describe the ruler, dynamic parameters describe what happens when the input moves, and timing parameters describe the clock. Definition: An ADC turns a voltage into a number. It does it in three steps, repeated on every tick of a clock: hold the voltage still, compare it against a ruler with 2ᴺ marks, and write down the mark number in binary. Analogy: Measuring a child’s height: ask them to stand still, line them up against a marked ruler, write the number in the book. Repeat every birthday. Example (A 12-bit, 100 MSPS converter): 4096 marks on the ruler, one reading every 10 ns; Output: 100 million 12-bit words per second = 1.2 Gbit/s; Every parameter in this talk describes how well one of those three steps is done.

## Slide 3
The parameter map
Opening
3
Datasheet numbers fall into five families. Knowing which family a parameter belongs to tells you when it will bite you.
Static (DC)
Measuring slow or steady voltages
Resolution N
Full-scale range
LSB
Offset error
Gain error
DNL
INL
Missing codes
Monotonicity
TUE
Drift
PSRR
CMRR
Dynamic (AC)
Any signal that moves: radio, audio, vibration
SNR
THD
HD2 / HD3
SINAD
ENOB
SFDR
IMD
Input-referred noise
Noise-free bits
Dynamic range
Timing
Fast inputs, control loops, interleaving
Sample rate
Conversion time
Latency
Aperture delay
Aperture jitter
Acquisition time
Settling time
Slew rate
Overvoltage recovery
Bandwidth
Undersampling, wideband or high-IF work
Analog bandwidth
Full-power bandwidth
Full-linear bandwidth
Oversampling ratio
Decimation
Power and system
Budgets, board design, multi-channel
Power dissipation
Supply voltages
Walden FoM
Schreier FoM
Crosstalk
Output coding
Digital interface
Notes: Point at each family and say when it matters: static for DC measurement, dynamic for signals, timing for fast inputs, bandwidth for undersampling, power for the budget. Definition: Datasheet numbers fall into five families. Knowing which family a parameter belongs to tells you when it will bite you.

## Slide 4
Part 1
Resolution and the transfer function
How fine the ruler is, and what one step is worth
12 minutes
4
Notes: The foundation: everything later is measured in LSBs.

## Slide 5
Resolution
Part 1 · Resolution and the transfer function
5
N · bits
How many binary digits the output word has. It fixes how many different levels the converter can report: 2ᴺ of them. It says nothing about how accurate those levels are — that is what every other parameter is for.
number of levels = 2ᴺ
8 bits → 256 levels, 12 bits → 4096, 16 bits → 65 536
Chart: resolution N (bits)
| 8 | 10 | 12 | 14 | 16 | 18 | 20 | 24
ideal SNR (dB) | 49.92 | 61.96 | 74 | 86.04 | 98.08 | 110.12 | 122.16 | 146.24
Resolution is the headline number and the most over-trusted one. A "16-bit" part delivering 12.5 effective bits is a 12.5-bit part.
≈
Think of it like this The number of marks on a ruler. A ruler with millimetre marks is not automatically accurate — the marks could still be printed in the wrong places.
EXAMPLE
Adding one bit
12 bits: 4096 levels, step 488 µV over 2 V
13 bits: 8192 levels, step 244 µV
Each bit doubles the levels, halves the step, and buys about 6 dB
Notes: Definition: How many binary digits the output word has. It fixes how many different levels the converter can report: 2ᴺ of them. It says nothing about how accurate those levels are — that is what every other parameter is for. Analogy: The number of marks on a ruler. A ruler with millimetre marks is not automatically accurate — the marks could still be printed in the wrong places. Example (Adding one bit): 12 bits: 4096 levels, step 488 µV over 2 V; 13 bits: 8192 levels, step 244 µV; Each bit doubles the levels, halves the step, and buys about 6 dB. Why it matters: Resolution is the headline number and the most over-trusted one. A "16-bit" part delivering 12.5 effective bits is a 12.5-bit part.

## Slide 6
Full-scale range
Part 1 · Resolution and the transfer function
6
V_FS, FSR · V
The span of input voltage between the lowest code and the highest. Drive the input outside it and the output clips: the top of the wave is flattened and the spectrum fills with harmonics that were never in the signal.
FSR = V_ref⁺ − V_ref⁻
Often just V_ref, or 2 × V_ref for a differential input
headroom (dBFS) = 20 log₁₀( V_in,pk / (FSR/2) )
How far below full scale you are running
Chart: time · dashed limits are ±full scale
Most in-the-field ADC failures are clipping, not noise. Radio front ends normally leave 6 to 12 dB of headroom for signal peaks.
≈
Think of it like this The length of the ruler. A 2-metre ruler cannot measure a 3-metre pole; it just reads "2 m" and you never learn the truth.
EXAMPLE
Leaving headroom
FSR 2 V peak-to-peak, so ±1 V
Drive to ±0.9 V: 0.9 dB of back-off, no clipping
Drive to ±1.2 V: clipped, and SFDR collapses from 80 dB to about 20 dB
Notes: Definition: The span of input voltage between the lowest code and the highest. Drive the input outside it and the output clips: the top of the wave is flattened and the spectrum fills with harmonics that were never in the signal. Analogy: The length of the ruler. A 2-metre ruler cannot measure a 3-metre pole; it just reads "2 m" and you never learn the truth. Example (Leaving headroom): FSR 2 V peak-to-peak, so ±1 V; Drive to ±0.9 V: 0.9 dB of back-off, no clipping; Drive to ±1.2 V: clipped, and SFDR collapses from 80 dB to about 20 dB. Why it matters: Most in-the-field ADC failures are clipping, not noise. Radio front ends normally leave 6 to 12 dB of headroom for signal peaks.

## Slide 7
LSB — the size of one step
Part 1 · Resolution and the transfer function
7
q, LSB · V
The voltage difference between two neighbouring codes. It is the natural unit for almost every other parameter on the datasheet: offset, DNL, INL and noise are all quoted in LSBs rather than volts, so they stay meaningful when the range changes.
LSB = FSR / 2ᴺ
The quantum: nothing smaller than this can be resolved
Chart: input (V) · 2 V range, LSB = 250 mV
Once the LSB drops below the noise of the circuitry in front of the ADC, extra bits buy nothing at all.
≈
Think of it like this The distance between two marks on the ruler. Everything else on the datasheet is measured in "how many marks wrong".
EXAMPLE
Same converter, three ranges
12 bit over 2 V: LSB = 2 / 4096 = 488 µV
12 bit over 5 V: LSB = 1.22 mV
16 bit over 2 V: LSB = 30.5 µV — smaller than most op-amp offsets
Notes: Definition: The voltage difference between two neighbouring codes. It is the natural unit for almost every other parameter on the datasheet: offset, DNL, INL and noise are all quoted in LSBs rather than volts, so they stay meaningful when the range changes. Analogy: The distance between two marks on the ruler. Everything else on the datasheet is measured in "how many marks wrong". Example (Same converter, three ranges): 12 bit over 2 V: LSB = 2 / 4096 = 488 µV; 12 bit over 5 V: LSB = 1.22 mV; 16 bit over 2 V: LSB = 30.5 µV — smaller than most op-amp offsets. Why it matters: Once the LSB drops below the noise of the circuitry in front of the ADC, extra bits buy nothing at all.

## Slide 8
Quantisation error
Part 1 · Resolution and the transfer function
8
e_q · LSB
The difference between the real input and the level the ADC reported. Rounding to the nearest mark means the error is never more than half a step, and on a busy signal it is as often up as down — so we treat it as a small extra noise.
−½ LSB ≤ e_q < +½ LSB
The error can never exceed half a step
Chart: input (V) · error never leaves ±½ LSB
≈
Think of it like this Rounding every price to the nearest 10p. Sometimes you gain 5p, sometimes you lose 5p, and over a month it averages out like small random noise.
EXAMPLE
12-bit, 2 V range
LSB 488 µV, so the error stays within ±244 µV
rms error = 488 µV / √12 = 141 µV
Against a 0.7 V rms full-scale sine that is 74 dB down
Notes: Definition: The difference between the real input and the level the ADC reported. Rounding to the nearest mark means the error is never more than half a step, and on a busy signal it is as often up as down — so we treat it as a small extra noise. Analogy: Rounding every price to the nearest 10p. Sometimes you gain 5p, sometimes you lose 5p, and over a month it averages out like small random noise. Example (12-bit, 2 V range): LSB 488 µV, so the error stays within ±244 µV; rms error = 488 µV / √12 = 141 µV; Against a 0.7 V rms full-scale sine that is 74 dB down. For the experts: The uniform, white model breaks for very small or exactly periodic inputs, where the error becomes a deterministic pattern that shows up as spurs. Dither — deliberately adding a little noise before the quantiser — randomises it and restores the model.

## Slide 9
Output coding
Part 1 · Resolution and the transfer function
9
How the level number is written down in binary. It changes nothing about accuracy, but getting it wrong turns a clean sine into a waveform that jumps violently through mid-scale.
Straight binary: 0 … 2ᴺ−1, natural for unipolar inputs
Offset binary: mid-scale is 1000…0, so zero volts is the middle code
Two’s complement: offset binary with the top bit inverted; negative numbers are negative
Gray code: only one bit changes between neighbours, so a mistimed read cannot produce a wildly wrong value
Input | Straight binary | Two’s complement
+ full scale | 1111 1111 | 0111 1111
mid-scale | 1000 0000 | 0000 0000
− full scale | 0000 0000 | 1000 0000
This is a five-minute bug that costs a day. Check the coding before you debug the analogue.
≈
Think of it like this The same measurement written in different notations. "Minus three" and "3 below zero" are the same height; a reader expecting one and given the other gets nonsense.
EXAMPLE
Mid-scale on a 12-bit part
Straight binary: 2048 = 1000 0000 0000
Two’s complement: 0 = 0000 0000 0000
Read two’s complement as straight binary and every negative sample looks like a huge positive one
Notes: Definition: How the level number is written down in binary. It changes nothing about accuracy, but getting it wrong turns a clean sine into a waveform that jumps violently through mid-scale. Analogy: The same measurement written in different notations. "Minus three" and "3 below zero" are the same height; a reader expecting one and given the other gets nonsense. Example (Mid-scale on a 12-bit part): Straight binary: 2048 = 1000 0000 0000; Two’s complement: 0 = 0000 0000 0000; Read two’s complement as straight binary and every negative sample looks like a huge positive one. Why it matters: This is a five-minute bug that costs a day. Check the coding before you debug the analogue.

## Slide 10
Reference voltage and its drift
Part 1 · Resolution and the transfer function
10
V_ref, ppm/°C · V, ppm/°C
Every ADC measures its input as a fraction of a reference. The converter can only ever be as accurate as that reference, so reference error appears directly as gain error, and reference drift appears as gain drift over temperature.
code ≈ 2ᴺ × V_in / V_ref
The reading is a ratio, not an absolute measurement
Chart: temperature (°C)
| -40 | -30 | -20 | -10 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90
2 ppm/°C | -8.5197 | -7.209 | -5.8982 | -4.5875 | -3.2768 | -1.9661 | -0.65536 | 0.65536 | 1.9661 | 3.2768 | 4.5875 | 5.8982 | 7.209 | 8.5197
10 ppm/°C | -42.5984 | -36.0448 | -29.4912 | -22.9376 | -16.384 | -9.8304 | -3.2768 | 3.2768 | 9.8304 | 16.384 | 22.9376 | 29.4912 | 36.0448 | 42.5984
50 ppm/°C | -212.992 | -180.224 | -147.456 | -114.688 | -81.92 | -49.152 | -16.384 | 16.384 | 49.152 | 81.92 | 114.688 | 147.456 | 180.224 | 212.992
For any converter above 12 bits, the reference is usually the accuracy limit, not the converter. Noise on the reference also lands straight in the result.
≈
Think of it like this A ruler made of metal. It measures perfectly at 20 °C, but on a hot day the whole ruler has stretched and every reading is proportionally wrong.
EXAMPLE
How many bits does drift cost?
16-bit part: 1 LSB = 1/65 536 = 15 ppm of full scale
A 10 ppm/°C reference over 50 °C drifts 500 ppm
That is 33 LSB — five bits of accuracy lost to temperature alone
Notes: Definition: Every ADC measures its input as a fraction of a reference. The converter can only ever be as accurate as that reference, so reference error appears directly as gain error, and reference drift appears as gain drift over temperature. Analogy: A ruler made of metal. It measures perfectly at 20 °C, but on a hot day the whole ruler has stretched and every reading is proportionally wrong. Example (How many bits does drift cost?): 16-bit part: 1 LSB = 1/65 536 = 15 ppm of full scale; A 10 ppm/°C reference over 50 °C drifts 500 ppm; That is 33 LSB — five bits of accuracy lost to temperature alone. Why it matters: For any converter above 12 bits, the reference is usually the accuracy limit, not the converter. Noise on the reference also lands straight in the result.

## Slide 11
Recap · the ruler itself
✓
Resolution N sets the number of marks: 2ᴺ. It promises nothing about accuracy
✓
Full-scale range is the length of the ruler; going past it clips and sprays harmonics
✓
LSB = FSR / 2ᴺ is the unit every other parameter is quoted in
✓
Quantisation error is at most half an LSB and behaves like noise of power LSB²/12
✓
The reading is a ratio to V_ref, so reference error and drift are your error and drift
11
Notes: No notes.

## Slide 12
Part 2
Static accuracy (DC)
Are the marks in the right places? The DC parameters
16 minutes
12
Notes: These four — offset, gain, DNL, INL — describe the shape of the staircase.

## Slide 13
Offset error
Part 2 · Static accuracy (DC)
13
E_O · LSB or mV
The whole staircase is shifted sideways: with zero volts in, the ADC does not report the zero code. Every reading is wrong by the same amount, in the same direction.
E_O = (first actual transition) − (first ideal transition)
Measured at the bottom of the range, in LSB
Chart: input (V) · the whole staircase slides sideways
Easy to remove: measure it once at zero input and subtract it in software. It matters most for small DC signals, and not at all for AC signals, where it…
≈
Think of it like this A bathroom scale that reads 2 kg with nobody standing on it. Every weight it reports is 2 kg too high, and you can fix it by turning the little wheel.
EXAMPLE
A 5 LSB offset on a 12-bit, 2 V part
5 × 488 µV = 2.44 mV added to every reading
Measuring a 10 mV sensor signal: a 24 % error
Measuring a 1 V signal: a 0.24 % error — the same offset, far less harm
Notes: Definition: The whole staircase is shifted sideways: with zero volts in, the ADC does not report the zero code. Every reading is wrong by the same amount, in the same direction. Analogy: A bathroom scale that reads 2 kg with nobody standing on it. Every weight it reports is 2 kg too high, and you can fix it by turning the little wheel. Example (A 5 LSB offset on a 12-bit, 2 V part): 5 × 488 µV = 2.44 mV added to every reading; Measuring a 10 mV sensor signal: a 24 % error; Measuring a 1 V signal: a 0.24 % error — the same offset, far less harm. Why it matters: Easy to remove: measure it once at zero input and subtract it in software. It matters most for small DC signals, and not at all for AC signals, where it only shifts bin 0 of the FFT.

## Slide 14
Gain error
Part 2 · Static accuracy (DC)
14
E_G · % FS or LSB
The staircase has the right starting point but the wrong slope, so the error grows the further up the range you go. Usually the reference is the culprit.
E_G = (actual slope / ideal slope) − 1
Quoted as a percentage of full scale, or in LSB at full scale
Chart: input (V) · right at zero, worst at the ends
Also correctable in software with a two-point calibration: measure near zero and near full scale, then fit a straight line. What calibration cannot fix…
≈
Think of it like this A tailor’s tape measure that has stretched. It still starts at zero, but by the far end everything reads short by a fixed proportion.
EXAMPLE
0.5 % gain error, 12-bit
At mid-scale (2048): error 10 LSB
At full scale (4095): error 20 LSB
At zero: no error at all — that is what distinguishes it from offset
Notes: Definition: The staircase has the right starting point but the wrong slope, so the error grows the further up the range you go. Usually the reference is the culprit. Analogy: A tailor’s tape measure that has stretched. It still starts at zero, but by the far end everything reads short by a fixed proportion. Example (0.5 % gain error, 12-bit): At mid-scale (2048): error 10 LSB; At full scale (4095): error 20 LSB; At zero: no error at all — that is what distinguishes it from offset. Why it matters: Also correctable in software with a two-point calibration: measure near zero and near full scale, then fit a straight line. What calibration cannot fix is drift.

## Slide 15
DNL — differential non-linearity
Part 2 · Static accuracy (DC)
15
DNL · LSB
How much wider or narrower each individual step is than one ideal LSB. It is a local measure: one bad step among 4095 good ones still counts.
DNL(k) = (actual width of code k) / LSB − 1
Zero means every step is exactly one LSB wide
Chart: code · each bar is one step’s width error
DNL is the noise-like part of static error: it adds directly to the noise floor and generates spurs, so it hurts AC performance as well as DC.
≈
Think of it like this A ruler where the marks are not evenly spaced. Most centimetres are right, but one is 1.4 cm and the next is 0.6 cm.
EXAMPLE
Reading the spec
DNL = ±0.5 LSB: every step is between 0.5 and 1.5 LSB wide
DNL = −0.9 LSB: one step is only a tenth of an LSB wide — nearly invisible
DNL = −1.0 LSB: that code never appears at all (see the next slide)
Notes: Definition: How much wider or narrower each individual step is than one ideal LSB. It is a local measure: one bad step among 4095 good ones still counts. Analogy: A ruler where the marks are not evenly spaced. Most centimetres are right, but one is 1.4 cm and the next is 0.6 cm. Example (Reading the spec): DNL = ±0.5 LSB: every step is between 0.5 and 1.5 LSB wide; DNL = −0.9 LSB: one step is only a tenth of an LSB wide — nearly invisible; DNL = −1.0 LSB: that code never appears at all (see the next slide). Why it matters: DNL is the noise-like part of static error: it adds directly to the noise floor and generates spurs, so it hurts AC performance as well as DC.

## Slide 16
Missing codes and monotonicity
Part 2 · Static accuracy (DC)
16
Two guarantees that follow from DNL. A code is missing when DNL reaches −1 LSB: that output value can never occur, whatever the input. A converter is monotonic when a rising input can never produce a falling output.
DNL ≤ −1 LSB → missing code
The step has been squeezed to zero width
DNL > −1 LSB everywhere → guaranteed monotonic
The usual way the guarantee is stated
Chart: code · the −1 LSB bar is a code that never appears
"No missing codes" is a guarantee worth paying for in measurement work. "Monotonic" is essential in any feedback loop.
≈
Think of it like this A lift that never stops on the fourth floor. It works fine, but you can never get out there — and if it sometimes goes down when you press "up", nothing built on it can be trusted.
EXAMPLE
Why monotonicity is non-negotiable in a control loop
A servo raises its drive and reads the sensor back
A non-monotonic ADC reports a fall, so the loop pushes harder
The loop latches up or oscillates — the classic symptom of a non-monotonic converter
Notes: Definition: Two guarantees that follow from DNL. A code is missing when DNL reaches −1 LSB: that output value can never occur, whatever the input. A converter is monotonic when a rising input can never produce a falling output. Analogy: A lift that never stops on the fourth floor. It works fine, but you can never get out there — and if it sometimes goes down when you press "up", nothing built on it can be trusted. Example (Why monotonicity is non-negotiable in a control loop): A servo raises its drive and reads the sensor back; A non-monotonic ADC reports a fall, so the loop pushes harder; The loop latches up or oscillates — the classic symptom of a non-monotonic converter. Why it matters: "No missing codes" is a guarantee worth paying for in measurement work. "Monotonic" is essential in any feedback loop.

## Slide 17
INL — integral non-linearity
Part 2 · Static accuracy (DC)
17
INL · LSB
How far the whole staircase bends away from a straight line, once offset and gain have been taken out. Where DNL is local and jagged, INL is the smooth, long bow across the range — and it is the running sum of DNL.
INL(k) = Σ DNL up to k
Accumulated step errors
INL = (actual transition − ideal) / LSB
Endpoint method; the best-fit-line method gives about half the number
Chart: code
INL sets the distortion floor. If you need SFDR, buy INL. Note which definition the datasheet uses: endpoint or best-fit changes the number by a factor…
≈
Think of it like this A ruler that is gently bowed. Each individual centimetre looks fine, but by the middle the accumulated bend has you several millimetres out.
EXAMPLE
INL is what limits distortion
±2 LSB INL on a 14-bit part
The bow acts like a soft nonlinearity, so it makes harmonics
Typically caps SFDR around 80 – 85 dB no matter how good the noise is
Notes: Definition: How far the whole staircase bends away from a straight line, once offset and gain have been taken out. Where DNL is local and jagged, INL is the smooth, long bow across the range — and it is the running sum of DNL. Analogy: A ruler that is gently bowed. Each individual centimetre looks fine, but by the middle the accumulated bend has you several millimetres out. Example (INL is what limits distortion): ±2 LSB INL on a 14-bit part; The bow acts like a soft nonlinearity, so it makes harmonics; Typically caps SFDR around 80 – 85 dB no matter how good the noise is. Why it matters: INL sets the distortion floor. If you need SFDR, buy INL. Note which definition the datasheet uses: endpoint or best-fit changes the number by a factor of two. For the experts: Bowed INL (an even-order shape) produces mostly HD2; S-shaped INL (odd-order) produces mostly HD3. The shape of the INL plot predicts which harmonic will dominate the spectrum.

## Slide 18
Total unadjusted error
Part 2 · Static accuracy (DC)
18
TUE · LSB
The single worst-case number: every static error added together, with no calibration applied. It answers the only question that matters for an uncalibrated system — how far out can one reading possibly be?
TUE ≈ √( E_O² + E_G² + INL² + … )
Root-sum-square, if the errors are independent
TUE_worst = |E_O| + |E_G| + |INL| + ½
Straight sum: the pessimistic bound some datasheets quote
Chart: uncalibrated 12-bit converter
| offset | gain | INL | quantisation | RSS total | worst case
contribution (LSB) | 2 | 3 | 1.5 | 0.5 | 3.9 | 7
If you never calibrate, TUE is the only accuracy number that means anything. If you do calibrate, offset and gain drop out and INL plus drift dominate.
≈
Think of it like this Every source of measurement error in one number, the way a shipping estimate quotes the worst case rather than the average.
EXAMPLE
12-bit part, no calibration
Offset 2 LSB, gain 3 LSB, INL 1.5 LSB, quantisation 0.5 LSB
Root-sum-square: √(4 + 9 + 2.25 + 0.25) = 3.9 LSB
Worst case sum: 7 LSB — so trust about 9 of your 12 bits
Notes: Definition: The single worst-case number: every static error added together, with no calibration applied. It answers the only question that matters for an uncalibrated system — how far out can one reading possibly be? Analogy: Every source of measurement error in one number, the way a shipping estimate quotes the worst case rather than the average. Example (12-bit part, no calibration): Offset 2 LSB, gain 3 LSB, INL 1.5 LSB, quantisation 0.5 LSB; Root-sum-square: √(4 + 9 + 2.25 + 0.25) = 3.9 LSB; Worst case sum: 7 LSB — so trust about 9 of your 12 bits. Why it matters: If you never calibrate, TUE is the only accuracy number that means anything. If you do calibrate, offset and gain drop out and INL plus drift dominate.

## Slide 19
Temperature drift
Part 2 · Static accuracy (DC)
19
ppm/°C · ppm/°C or LSB/°C
Offset and gain both move with temperature. Calibration at 25 °C on the bench does nothing for a board that runs at 70 °C in a cabinet, so drift is the error that survives calibration.
error(T) = error(25 °C) + drift × (T − 25)
1 ppm of full scale = 0.065 LSB at 16 bits
Chart: temperature (°C) · calibrated at 25 °C
| -40 | -30 | -20 | -10 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
offset drift 1 µV/°C | 2.1311 | 1.8033 | 1.4754 | 1.1475 | 0.81967 | 0.4918 | 0.16393 | 0.16393 | 0.4918 | 0.81967 | 1.1475 | 1.4754 | 1.8033
gain drift 5 ppm/°C | 21.2992 | 18.0224 | 14.7456 | 11.4688 | 8.192 | 4.9152 | 1.6384 | 1.6384 | 4.9152 | 8.192 | 11.4688 | 14.7456 | 18.0224
For precision work, drift and reference stability usually beat resolution as the thing to spend money on.
≈
Think of it like this Calibrating your kitchen scale in a cold kitchen, then using it beside a hot oven. The calibration was honest; the conditions moved.
EXAMPLE
A 16-bit measurement over an industrial range
Gain drift 5 ppm/°C, range −40 to +85 °C, so ΔT = 60 °C from calibration
5 × 60 = 300 ppm = 19.7 LSB at 16 bits
Four bits gone, and no amount of room-temperature calibration recovers them
Notes: Definition: Offset and gain both move with temperature. Calibration at 25 °C on the bench does nothing for a board that runs at 70 °C in a cabinet, so drift is the error that survives calibration. Analogy: Calibrating your kitchen scale in a cold kitchen, then using it beside a hot oven. The calibration was honest; the conditions moved. Example (A 16-bit measurement over an industrial range): Gain drift 5 ppm/°C, range −40 to +85 °C, so ΔT = 60 °C from calibration; 5 × 60 = 300 ppm = 19.7 LSB at 16 bits; Four bits gone, and no amount of room-temperature calibration recovers them. Why it matters: For precision work, drift and reference stability usually beat resolution as the thing to spend money on.

## Slide 20
PSRR and CMRR
Part 2 · Static accuracy (DC)
20
PSRR, CMRR · dB
Two rejection ratios. PSRR says how much of a wobble on the supply rail leaks into the reading. CMRR says how much of a voltage common to both inputs of a differential converter leaks in, when in theory only the difference should count.
PSRR = 20 log₁₀( ΔV_supply / ΔV_error )
Higher is better
Chart: supply ripple frequency (Hz)
| 10 | 100 | 1 k | 10 k | 100 k | 1 M | 10 M
PSRR (dB) | 130 | 110 | 90 | 70 | 50 | 30 | 20
PSRR falls with frequency, so the number at DC is the flattering one. Check it at your switching regulator’s frequency.
≈
Think of it like this Trying to weigh something on a scale sitting on a washing machine. CMRR is how well the scale ignores the shaking; PSRR is how well it ignores a flickering mains supply.
EXAMPLE
Supply ripple leaking in
Switching regulator ripple: 20 mV at 500 kHz
ADC PSRR at 500 kHz: 60 dB → divide by 1000
20 µV of error — about 0.7 LSB on a 16-bit, 2 V part, and it shows as a spur at 500 kHz
Notes: Definition: Two rejection ratios. PSRR says how much of a wobble on the supply rail leaks into the reading. CMRR says how much of a voltage common to both inputs of a differential converter leaks in, when in theory only the difference should count. Analogy: Trying to weigh something on a scale sitting on a washing machine. CMRR is how well the scale ignores the shaking; PSRR is how well it ignores a flickering mains supply. Example (Supply ripple leaking in): Switching regulator ripple: 20 mV at 500 kHz; ADC PSRR at 500 kHz: 60 dB → divide by 1000; 20 µV of error — about 0.7 LSB on a 16-bit, 2 V part, and it shows as a spur at 500 kHz. Why it matters: PSRR falls with frequency, so the number at DC is the flattering one. Check it at your switching regulator’s frequency.

## Slide 21
Recap · static accuracy
✓
Offset: the staircase is shifted — same error everywhere, easy to calibrate out
✓
Gain: the staircase has the wrong slope — error grows with signal, two-point calibration fixes it
✓
DNL: each step the wrong width. At −1 LSB a code goes missing; above −1 everywhere means monotonic
✓
INL: the whole curve bows. It is the running sum of DNL, and it sets your distortion floor
✓
TUE bundles them all for an uncalibrated system; drift is what survives calibration
21
Notes: No notes.

## Slide 22
Part 3
Dynamic performance (AC)
What happens once the input starts moving
20 minutes
22
Notes: These are all measured the same way: apply a pure sine, take an FFT, and read the answer off the spectrum.

## Slide 23
SNR — signal-to-noise ratio
Part 3 · Dynamic performance (AC)
23
SNR · dB
How far the wanted tone stands above the noise, with the harmonics deliberately excluded. It is the parameter that tells you how small a signal you can still see.
SNR = 10 log₁₀( P_signal / P_noise )
Harmonics are removed from the noise sum first
SNR_ideal = 6.02 N + 1.76 dB
The best a perfect N-bit converter can manage
Chart: resolution (bits)
| 8 | 10 | 12 | 14 | 16 | 18
ideal 6.02N + 1.76 | 49.92 | 61.96 | 74 | 86.04 | 98.08 | 110.12
a typical real part | 47.92 | 59.26 | 70.6 | 81.94 | 93.28 | 104.62
Real SNR sits below the ideal because of thermal noise, clock jitter and DNL. The gap between them is the honest measure of an ADC’s quality.
≈
Think of it like this How loudly a voice stands out over the hiss of a room. Distortion is a separate problem — that is the voice being slurred, not drowned.
EXAMPLE
Where the ideal number comes from
Full-scale sine power: (FSR/2)²/2 = FSR²/8
Quantisation noise power: LSB²/12 = FSR²/(12 × 2²ᴺ)
Ratio = 1.5 × 2²ᴺ → 10 log₁₀ = 6.02 N + 1.76 dB
Notes: Definition: How far the wanted tone stands above the noise, with the harmonics deliberately excluded. It is the parameter that tells you how small a signal you can still see. Analogy: How loudly a voice stands out over the hiss of a room. Distortion is a separate problem — that is the voice being slurred, not drowned. Example (Where the ideal number comes from): Full-scale sine power: (FSR/2)²/2 = FSR²/8; Quantisation noise power: LSB²/12 = FSR²/(12 × 2²ᴺ); Ratio = 1.5 × 2²ᴺ → 10 log₁₀ = 6.02 N + 1.76 dB. Why it matters: Real SNR sits below the ideal because of thermal noise, clock jitter and DNL. The gap between them is the honest measure of an ADC’s quality.

## Slide 24
Input-referred noise and noise-free bits
Part 3 · Dynamic performance (AC)
24
σ_n, NFR · LSB rms, bits
Short the input and take thousands of readings: a perfect ADC returns the same code every time, a real one returns a small spread of codes. The width of that spread is input-referred noise, and it decides how many of your bits are actually trustworthy.
noise-free bits = log₂( 2ᴺ / (6.6 × σ_n) )
Peak-to-peak: codes that never flicker
Chart: output code, input shorted · σ = 1.9 LSB
| -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6
readings per code | 26 | 144 | 493 | 1210 | 2468 | 3652 | 4057 | 3582 | 2518 | 1222 | 455 | 136 | 34
This is why 24-bit converters are never 24-bit measurements. Datasheets often give a table of noise-free bits against output rate — that table is the…
≈
Think of it like this A bathroom scale whose last digit will not settle. It may display grams, but if that digit dances over five values, you do not have gram resolution.
EXAMPLE
A 24-bit delta-sigma part
Input-referred noise: 12 LSB rms
Noise-free bits = log₂(16 777 216 / 79) = 17.7
The other 6 bits are real outputs, but they only ever show noise
Notes: Definition: Short the input and take thousands of readings: a perfect ADC returns the same code every time, a real one returns a small spread of codes. The width of that spread is input-referred noise, and it decides how many of your bits are actually trustworthy. Analogy: A bathroom scale whose last digit will not settle. It may display grams, but if that digit dances over five values, you do not have gram resolution. Example (A 24-bit delta-sigma part): Input-referred noise: 12 LSB rms; Noise-free bits = log₂(16 777 216 / 79) = 17.7; The other 6 bits are real outputs, but they only ever show noise. Why it matters: This is why 24-bit converters are never 24-bit measurements. Datasheets often give a table of noise-free bits against output rate — that table is the honest specification.

## Slide 25
THD and the individual harmonics
Part 3 · Dynamic performance (AC)
25
THD, HD2, HD3 · dBc or %
A perfect converter fed one pure tone returns one pure tone. A real one bends the signal slightly, and the bend creates copies at exact multiples of the input frequency. THD adds up all those copies; HD2 and HD3 name the two that usually dominate.
THD = 10 log₁₀( (P₂ + P₃ + … + P₉) / P₁ )
Quoted in dBc: decibels relative to the carrier
Chart: frequency (fraction of f_s) · HD2 and HD3 marked by the peaks
Harmonics fold. A harmonic above f_s/2 comes back inside the band at a frequency that looks like a real signal, which is why a distortion problem often…
≈
Think of it like this A slightly buzzy loudspeaker. Play one clean note and you also hear faint notes an octave and an octave-and-a-fifth above it, which the recording never contained.
EXAMPLE
Reading a spectrum
Tone at 10 MHz, 0 dBFS. HD2 appears at 20 MHz, −72 dBc
HD3 at 30 MHz, −78 dBc
THD = 10 log₁₀(10⁻⁷·² + 10⁻⁷·⁸) = −70.9 dBc
Notes: Definition: A perfect converter fed one pure tone returns one pure tone. A real one bends the signal slightly, and the bend creates copies at exact multiples of the input frequency. THD adds up all those copies; HD2 and HD3 name the two that usually dominate. Analogy: A slightly buzzy loudspeaker. Play one clean note and you also hear faint notes an octave and an octave-and-a-fifth above it, which the recording never contained. Example (Reading a spectrum): Tone at 10 MHz, 0 dBFS. HD2 appears at 20 MHz, −72 dBc; HD3 at 30 MHz, −78 dBc; THD = 10 log₁₀(10⁻⁷·² + 10⁻⁷·⁸) = −70.9 dBc. Why it matters: Harmonics fold. A harmonic above f_s/2 comes back inside the band at a frequency that looks like a real signal, which is why a distortion problem often presents as a mystery spur. For the experts: Even harmonics come mainly from asymmetry between the two halves of a differential path; odd harmonics from symmetric compression. HD2 that improves when you balance the driver, and HD3 that worsens with amplitude, are the classic signatures.

## Slide 26
SINAD — signal to noise and distortion
Part 3 · Dynamic performance (AC)
26
SINAD, SNDR · dB
The honest one. SNR ignores harmonics, THD ignores noise; SINAD counts everything that is not the wanted tone. It is the number ENOB is calculated from.
SINAD = 10 log₁₀( P_signal / (P_noise + P_distortion) )
Always the smallest of the three ratios
Chart: SINAD is always below both
| SNR | THD (as a ratio) | SINAD
dB | 72 | 76 | 70.5
When a datasheet quotes SNR and SINAD close together, the part is noise-limited. When SINAD is far below SNR, it is distortion-limited — and the fix is…
≈
Think of it like this Judging a phone call by how much of it you actually understood, rather than measuring the hiss and the crackle separately.
EXAMPLE
Combining the two
SNR 72 dB, THD −76 dBc
SINAD = −10 log₁₀(10⁻⁷·² + 10⁻⁷·⁶) = 70.5 dB
The worse of the two dominates: fixing distortion alone would gain only 1.5 dB
Notes: Definition: The honest one. SNR ignores harmonics, THD ignores noise; SINAD counts everything that is not the wanted tone. It is the number ENOB is calculated from. Analogy: Judging a phone call by how much of it you actually understood, rather than measuring the hiss and the crackle separately. Example (Combining the two): SNR 72 dB, THD −76 dBc; SINAD = −10 log₁₀(10⁻⁷·² + 10⁻⁷·⁶) = 70.5 dB; The worse of the two dominates: fixing distortion alone would gain only 1.5 dB. Why it matters: When a datasheet quotes SNR and SINAD close together, the part is noise-limited. When SINAD is far below SNR, it is distortion-limited — and the fix is a different one.

## Slide 27
ENOB — effective number of bits
Part 3 · Dynamic performance (AC)
27
ENOB · bits
The resolution you actually got, obtained by running the ideal-SNR formula backwards on the measured SINAD. It converts a decibel figure into the only unit people intuitively understand: bits.
ENOB = ( SINAD − 1.76 ) / 6.02
For a full-scale input
ENOB = ( SINAD − 1.76 + back-off ) / 6.02
Add the dB you backed off, or you will under-report the part
Chart: input frequency (MHz)
| 1 | 5 | 10 | 20 | 50 | 70 | 100 | 150 | 200
ENOB of a "14-bit" part | 12.3 | 11.6849 | 11.42 | 11.1551 | 10.8049 | 10.6763 | 10.54 | 10.385 | 10.2751
headline resolution | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14
ENOB always falls as input frequency rises. A single ENOB number is meaningless without the frequency it was measured at.
≈
Think of it like this A car’s advertised top speed against the speed it reaches on a real road with a real load. ENOB is the road figure.
EXAMPLE
A "14-bit" converter at 70 MHz input
Measured SINAD: 68 dB, driven 1 dB below full scale
ENOB = (68 − 1.76 + 1) / 6.02 = 11.2 bits
Nearly three bits of the fourteen are not there at this frequency
Notes: Definition: The resolution you actually got, obtained by running the ideal-SNR formula backwards on the measured SINAD. It converts a decibel figure into the only unit people intuitively understand: bits. Analogy: A car’s advertised top speed against the speed it reaches on a real road with a real load. ENOB is the road figure. Example (A "14-bit" converter at 70 MHz input): Measured SINAD: 68 dB, driven 1 dB below full scale; ENOB = (68 − 1.76 + 1) / 6.02 = 11.2 bits; Nearly three bits of the fourteen are not there at this frequency. Why it matters: ENOB always falls as input frequency rises. A single ENOB number is meaningless without the frequency it was measured at.

## Slide 28
SFDR — spurious-free dynamic range
Part 3 · Dynamic performance (AC)
28
SFDR · dBc or dBFS
The gap between the wanted tone and the single largest unwanted spike anywhere in the spectrum, whether or not it is a harmonic. It answers one question exactly: how small a signal can I still find while a big one is present?
SFDR = 10 log₁₀( P_signal / P_largest spur )
dBc relative to the carrier, or dBFS relative to full scale
Chart: frequency · SFDR is the gap to the tallest spur
SFDR is the number radio engineers care about most, and it is often limited by INL rather than by noise. Averaging improves the noise floor but never…
≈
Think of it like this Trying to hear a whisper at a party while someone shouts. SFDR is how much quieter than the shout a whisper can be and still be picked out.
EXAMPLE
Why a radio receiver lives on SFDR
Wanted channel at −90 dBFS, a strong neighbour at −10 dBFS
You need 80 dB of SFDR just to see the wanted channel at all
A spur at −70 dBc from the strong signal would completely mask it
Notes: Definition: The gap between the wanted tone and the single largest unwanted spike anywhere in the spectrum, whether or not it is a harmonic. It answers one question exactly: how small a signal can I still find while a big one is present? Analogy: Trying to hear a whisper at a party while someone shouts. SFDR is how much quieter than the shout a whisper can be and still be picked out. Example (Why a radio receiver lives on SFDR): Wanted channel at −90 dBFS, a strong neighbour at −10 dBFS; You need 80 dB of SFDR just to see the wanted channel at all; A spur at −70 dBc from the strong signal would completely mask it. Why it matters: SFDR is the number radio engineers care about most, and it is often limited by INL rather than by noise. Averaging improves the noise floor but never improves SFDR.

## Slide 29
Intermodulation distortion
Part 3 · Dynamic performance (AC)
29
IMD2, IMD3, IP3 · dBc
Feed two tones instead of one and the nonlinearity mixes them together, producing sums and differences. The third-order products at 2f₁−f₂ and 2f₂−f₁ are the dangerous ones because they land right next to the originals, where no filter can remove them.
second order: f₂ ± f₁
Usually far away and filterable
Chart: bin · products at 2f₁−f₂ and 2f₂−f₁ sit beside the tones
Single-tone THD can look excellent while two-tone IMD is poor. Any receiver that must handle more than one signal at once should be specified on IMD,…
≈
Think of it like this Two singers slightly out of tune producing an audible beat note that neither of them is singing.
EXAMPLE
Two carriers 1 MHz apart
Tones at 10.0 and 11.0 MHz
Third-order products at 9.0 and 12.0 MHz — inside the same channel
At −75 dBc they set the floor for any weak signal nearby
Notes: Definition: Feed two tones instead of one and the nonlinearity mixes them together, producing sums and differences. The third-order products at 2f₁−f₂ and 2f₂−f₁ are the dangerous ones because they land right next to the originals, where no filter can remove them. Analogy: Two singers slightly out of tune producing an audible beat note that neither of them is singing. Example (Two carriers 1 MHz apart): Tones at 10.0 and 11.0 MHz; Third-order products at 9.0 and 12.0 MHz — inside the same channel; At −75 dBc they set the floor for any weak signal nearby. Why it matters: Single-tone THD can look excellent while two-tone IMD is poor. Any receiver that must handle more than one signal at once should be specified on IMD, not THD.

## Slide 30
FFT noise floor and processing gain
Part 3 · Dynamic performance (AC)
30
The noise floor you see on an FFT plot is not the converter’s SNR. The total noise is spread across N/2 bins, so each bin holds only a fraction of it. Taking a longer transform pushes the visible floor down without the converter improving at all.
floor = −SNR − 10 log₁₀( N/2 )
Per-bin level, in dBFS
Chart: FFT length · the same 12-bit converter every time
| 256 | 512 | 1024 | 2048 | 4096 | 8192
visible floor (dBFS) | -95.0721 | -98.0824 | -101.0927 | -104.103 | -107.1133 | -110.1236
Never compare noise floors from FFTs of different lengths. This is the most common way ADC plots are made to look better than they are.
≈
Think of it like this Spreading a fixed amount of butter over more and more slices of bread. There is no more butter; each slice just gets less.
EXAMPLE
12-bit part, 4096-point FFT
SNR 74 dB, processing gain 10 log₁₀(2048) = 33 dB
Visible floor: −107 dBFS
Change to a 256-point FFT and the same converter shows −95 dBFS
Notes: Definition: The noise floor you see on an FFT plot is not the converter’s SNR. The total noise is spread across N/2 bins, so each bin holds only a fraction of it. Taking a longer transform pushes the visible floor down without the converter improving at all. Analogy: Spreading a fixed amount of butter over more and more slices of bread. There is no more butter; each slice just gets less. Example (12-bit part, 4096-point FFT): SNR 74 dB, processing gain 10 log₁₀(2048) = 33 dB; Visible floor: −107 dBFS; Change to a 256-point FFT and the same converter shows −95 dBFS. Why it matters: Never compare noise floors from FFTs of different lengths. This is the most common way ADC plots are made to look better than they are.

## Slide 31
Dynamic range
Part 3 · Dynamic performance (AC)
31
DR · dB
The span between the largest signal the converter can take without clipping and the smallest it can still distinguish from noise. It is what decides whether you need an automatic gain control in front of it.
DR = 20 log₁₀( largest / smallest )
For a converter with no oversampling, DR ≈ SNR
Chart: oversampling ratio
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
plain oversampling | 74 | 77.0103 | 80.0206 | 83.0309 | 86.0412 | 89.0515 | 92.0618 | 95.0721
1st-order shaping | 74 | 83 | 92 | 101 | 110 | 119 | 128 | 137
2nd-order shaping | 74 | 89 | 104 | 119 | 134 | 149 | 164 | 179
Oversampling buys dynamic range that resolution alone does not: every doubling of the sample rate adds 3 dB, and a noise-shaping loop adds far more.
≈
Think of it like this A camera photographing a room with a bright window. Dynamic range is whether you can see detail in the sunlit street and in the shadowy corner in one shot.
EXAMPLE
Wi-Fi receiver
Strongest signal at the ADC: −10 dBFS. Weakest wanted: −80 dBFS
Needs 70 dB of usable range, so a 12-bit part with 74 dB SNR just fits
Add a 20 dB fade margin and you need 14 bits, or an AGC
Notes: Definition: The span between the largest signal the converter can take without clipping and the smallest it can still distinguish from noise. It is what decides whether you need an automatic gain control in front of it. Analogy: A camera photographing a room with a bright window. Dynamic range is whether you can see detail in the sunlit street and in the shadowy corner in one shot. Example (Wi-Fi receiver): Strongest signal at the ADC: −10 dBFS. Weakest wanted: −80 dBFS; Needs 70 dB of usable range, so a 12-bit part with 74 dB SNR just fits; Add a 20 dB fade margin and you need 14 bits, or an AGC. Why it matters: Oversampling buys dynamic range that resolution alone does not: every doubling of the sample rate adds 3 dB, and a noise-shaping loop adds far more.

## Slide 32
Recap · dynamic performance
✓
SNR: tone above the noise, harmonics excluded. Ideal is 6.02 N + 1.76 dB
✓
THD: all the harmonics added up; HD2 and HD3 usually dominate
✓
SINAD counts noise and distortion together — it is the honest one
✓
ENOB = (SINAD − 1.76 + back-off) / 6.02, and it always falls with input frequency
✓
SFDR is the biggest single spur: the number that decides if you can see a weak signal beside a strong one
✓
The FFT floor is not the SNR — subtract the processing gain of 10 log₁₀(N/2)
32
Notes: No notes.

## Slide 33
Part 4
Speed and timing
The clock, and everything that has to finish before the next tick
14 minutes
33
Notes: Timing parameters are the ones that silently destroy a high-frequency measurement.

## Slide 34
Sampling rate and throughput
Part 4 · Speed and timing
34
f_s · SPS
How many complete conversions the ADC delivers per second. Nyquist sets the floor: you must sample faster than twice the highest frequency present, or fast signals come back disguised as slow ones and no processing can undo it.
f_s > 2 × f_max
Nyquist. In practice 2.2 to 2.5×, to leave the anti-alias filter room
f_alias = | f − k f_s |
Where a too-fast tone reappears
Chart: input tone, sampled at 100 MSPS · limit is 50 MHz
| 10 MHz | 30 MHz | 45 MHz | 60 MHz | 80 MHz | 110 MHz | 140 MHz
where it appears (MHz) | 10 | 30 | 45 | 40 | 20 | 10 | 40
Multiplexed converters share one core between channels, so the per-channel rate is the throughput divided by the channel count. Check which number the…
≈
Think of it like this A film camera at 24 frames a second. Spokes on a wheel spinning faster than that appear to turn backwards, and the footage cannot be repaired afterwards.
EXAMPLE
A 60 MHz tone at 100 MSPS
Nyquist limit: 50 MHz
The tone appears at |60 − 100| = 40 MHz
It looks exactly like a genuine 40 MHz signal — nothing marks it as fake
Notes: Definition: How many complete conversions the ADC delivers per second. Nyquist sets the floor: you must sample faster than twice the highest frequency present, or fast signals come back disguised as slow ones and no processing can undo it. Analogy: A film camera at 24 frames a second. Spokes on a wheel spinning faster than that appear to turn backwards, and the footage cannot be repaired afterwards. Example (A 60 MHz tone at 100 MSPS): Nyquist limit: 50 MHz; The tone appears at |60 − 100| = 40 MHz; It looks exactly like a genuine 40 MHz signal — nothing marks it as fake. Why it matters: Multiplexed converters share one core between channels, so the per-channel rate is the throughput divided by the channel count. Check which number the datasheet quotes.

## Slide 35
Conversion time and latency
Part 4 · Speed and timing
35
t_conv, latency · s, cycles
Two different things that are easy to confuse. Conversion time is how long one measurement takes. Latency is how long you wait before that particular sample appears at the output — in a pipeline converter, several samples are in flight at once.
throughput = 1 / t_conv, but latency may be many cycles
A pipeline delivers a sample every cycle, each one several cycles old
Architecture | Result rate | Latency
SAR | one per N clocks | none
Pipeline | one per clock | 8 – 16 clocks
Flash | one per clock | 1 clock
Delta-sigma | one per OSR clocks | hundreds of clocks
Latency is irrelevant for spectrum analysis and fatal in a fast control loop, where it becomes phase lag and eats your stability margin.
≈
Think of it like this A car factory rolls out one car a minute, but any individual car spent eight hours on the line. Throughput and latency are not the same measurement.
EXAMPLE
Architecture decides latency
SAR: N clock cycles, result available immediately after — latency ≈ 0
Pipeline: one result per clock, but 8 to 16 cycles behind the input
Delta-sigma: hundreds of cycles, because of the decimation filter
Notes: Definition: Two different things that are easy to confuse. Conversion time is how long one measurement takes. Latency is how long you wait before that particular sample appears at the output — in a pipeline converter, several samples are in flight at once. Analogy: A car factory rolls out one car a minute, but any individual car spent eight hours on the line. Throughput and latency are not the same measurement. Example (Architecture decides latency): SAR: N clock cycles, result available immediately after — latency ≈ 0; Pipeline: one result per clock, but 8 to 16 cycles behind the input; Delta-sigma: hundreds of cycles, because of the decimation filter. Why it matters: Latency is irrelevant for spectrum analysis and fatal in a fast control loop, where it becomes phase lag and eats your stability margin.

## Slide 36
Aperture delay
Part 4 · Speed and timing
36
t_AD · s
The fixed gap between the clock edge arriving and the sampling switch actually opening. Because it is fixed and repeatable, it is harmless in a single converter — it just shifts the time axis slightly.
sample instant = clock edge + t_AD
Constant, and therefore calibratable
Chart: delay mismatch between interleaved channels (ps)
| 1 | 2 | 5 | 10 | 20 | 50 | 100 | 200
f_in = 100 MHz | -70.057 | -64.0364 | -56.0776 | -50.057 | -44.0364 | -36.0776 | -30.057 | -24.0364
f_in = 500 MHz | -56.0776 | -50.057 | -42.0982 | -36.0776 | -30.057 | -22.0982 | -16.0776 | -10.057
Fixed delay is fine. Mismatch between channels is not — it is the main reason interleaved converters need calibration.
≈
Think of it like this A camera with a shutter that always fires exactly 20 ms after you press the button. Predictable, so you simply press 20 ms early.
EXAMPLE
When it does matter
Two ADCs interleaved to double the rate must sample exactly half a period apart
A 200 ps aperture-delay mismatch at 500 MSPS is a 10 % timing error
The result is an interleaving spur at f_s/2 − f_in
Notes: Definition: The fixed gap between the clock edge arriving and the sampling switch actually opening. Because it is fixed and repeatable, it is harmless in a single converter — it just shifts the time axis slightly. Analogy: A camera with a shutter that always fires exactly 20 ms after you press the button. Predictable, so you simply press 20 ms early. Example (When it does matter): Two ADCs interleaved to double the rate must sample exactly half a period apart; A 200 ps aperture-delay mismatch at 500 MSPS is a 10 % timing error; The result is an interleaving spur at f_s/2 − f_in. Why it matters: Fixed delay is fine. Mismatch between channels is not — it is the main reason interleaved converters need calibration.

## Slide 37
Aperture jitter
Part 4 · Speed and timing
37
t_j · s rms
The random, cycle-to-cycle variation in when the switch opens. A fast-moving input travels a long way during that uncertainty, so the frozen value is wrong. Above a certain input frequency, jitter — not resolution — sets your accuracy.
SNR_jitter = −20 log₁₀( 2π f_in t_j )
Depends on the input frequency, not the sample rate
Chart: input frequency (MHz)
| 1 | 3 | 10 | 30 | 100 | 300 | 1000
100 fs | 124.0364 | 114.494 | 104.0364 | 94.494 | 84.0364 | 74.494 | 64.0364
1 ps | 104.0364 | 94.494 | 84.0364 | 74.494 | 64.0364 | 54.494 | 44.0364
10 ps | 84.0364 | 74.494 | 64.0364 | 54.494 | 44.0364 | 34.494 | 24.0364
Jitter comes from the clock source as much as the ADC. Undersampling a high IF is exactly the case where jitter dominates, because the formula uses the…
≈
Think of it like this Photographing a sprinter with a shutter that fires a little early or late each time. The faster the runner, the more the same timing slip blurs the picture.
EXAMPLE
The budget at 200 MHz
1 ps rms jitter: SNR limit = −20 log₁₀(2π × 2e8 × 1e−12) = 58 dB
That caps you at 9.3 effective bits, whatever the part claims
For 12 bits at 200 MHz you need about 160 fs — total, clock plus converter
Notes: Definition: The random, cycle-to-cycle variation in when the switch opens. A fast-moving input travels a long way during that uncertainty, so the frozen value is wrong. Above a certain input frequency, jitter — not resolution — sets your accuracy. Analogy: Photographing a sprinter with a shutter that fires a little early or late each time. The faster the runner, the more the same timing slip blurs the picture. Example (The budget at 200 MHz): 1 ps rms jitter: SNR limit = −20 log₁₀(2π × 2e8 × 1e−12) = 58 dB; That caps you at 9.3 effective bits, whatever the part claims; For 12 bits at 200 MHz you need about 160 fs — total, clock plus converter. Why it matters: Jitter comes from the clock source as much as the ADC. Undersampling a high IF is exactly the case where jitter dominates, because the formula uses the input frequency. For the experts: Total jitter is the root-sum-square of the converter’s own aperture jitter and the clock’s integrated phase noise over the relevant offset band. Halving one when the other dominates buys nothing.

## Slide 38
Acquisition and settling time
Part 4 · Speed and timing
38
t_acq, t_s · s
During the track phase the hold capacitor has to charge to within half an LSB of the input. More bits means a tighter target and therefore more time constants — and this is what sets the demands on whatever amplifier drives the converter.
error = FSR × e^(−t/τ)
Single-pole settling
Chart: time constants elapsed · 16 bits needs 11.8
Under-settling looks exactly like distortion in the FFT, because the error depends on how far the input moved. Most "the ADC is bad" reports are really…
≈
Think of it like this Filling a measuring jug from a tap. Getting roughly full is quick; getting to the exact line, with the surface completely still, takes far longer.
EXAMPLE
Driving a 16-bit SAR at 1 MSPS
Track time available: about 500 ns
16 bits needs 11.8 time constants, so τ < 42 ns
That means an amplifier bandwidth above 3.8 MHz, settling to 0.0008 % — not a casual op-amp
Notes: Definition: During the track phase the hold capacitor has to charge to within half an LSB of the input. More bits means a tighter target and therefore more time constants — and this is what sets the demands on whatever amplifier drives the converter. Analogy: Filling a measuring jug from a tap. Getting roughly full is quick; getting to the exact line, with the surface completely still, takes far longer. Example (Driving a 16-bit SAR at 1 MSPS): Track time available: about 500 ns; 16 bits needs 11.8 time constants, so τ < 42 ns; That means an amplifier bandwidth above 3.8 MHz, settling to 0.0008 % — not a casual op-amp. Why it matters: Under-settling looks exactly like distortion in the FFT, because the error depends on how far the input moved. Most "the ADC is bad" reports are really driver settling.

## Slide 39
Slew rate and overvoltage recovery
Part 4 · Speed and timing
39
SR, t_rec · V/µs, s
Slew rate is how fast the driving circuit can move its output; if the signal demands more, the peaks are flattened and the spectrum fills with harmonics. Overvoltage recovery is how long the input takes to behave again after being driven past full scale.
SR_needed = π × FSR × f
Peak slope of a full-scale sine
Chart: signal frequency · full-scale sine into a 2 V range
| 1 MHz | 5 MHz | 10 MHz | 25 MHz | 50 MHz | 100 MHz
slew rate needed (V/µs) | 6.2832 | 31.4159 | 62.8319 | 157.0796 | 314.1593 | 628.3185
Overvoltage recovery matters in radar and pulsed systems, where a huge blocking signal is followed immediately by the tiny echo you actually want.
≈
Think of it like this A speedometer needle that cannot swing fast enough. Slam the accelerator and it lags, so the trace you record is a flattened version of what really happened.
EXAMPLE
A 2 V range at 50 MHz
SR needed = π × 2 × 50e6 = 314 V/µs
A 100 V/µs op-amp will visibly flatten the peaks
The FFT shows this as HD3 rising steeply with amplitude
Notes: Definition: Slew rate is how fast the driving circuit can move its output; if the signal demands more, the peaks are flattened and the spectrum fills with harmonics. Overvoltage recovery is how long the input takes to behave again after being driven past full scale. Analogy: A speedometer needle that cannot swing fast enough. Slam the accelerator and it lags, so the trace you record is a flattened version of what really happened. Example (A 2 V range at 50 MHz): SR needed = π × 2 × 50e6 = 314 V/µs; A 100 V/µs op-amp will visibly flatten the peaks; The FFT shows this as HD3 rising steeply with amplitude. Why it matters: Overvoltage recovery matters in radar and pulsed systems, where a huge blocking signal is followed immediately by the tiny echo you actually want.

## Slide 40
Recap · speed and timing
✓
f_s must exceed 2 × the highest frequency present, or tones fold and cannot be recovered
✓
Conversion time is not latency: a pipeline gives one result per clock, each many clocks old
✓
Aperture delay is fixed and harmless; mismatch between interleaved channels is not
✓
Aperture jitter limits SNR to −20 log₁₀(2π f_in t_j) — set by input frequency, not sample rate
✓
Settling to N bits needs ln(2^(N+1)) time constants; under-settling looks exactly like distortion
40
Notes: No notes.

## Slide 41
Part 5
Bandwidth and sampling
What the input can accept, and what the clock can keep up with
10 minutes
41
Notes: Analog bandwidth and sample rate are separate specifications, and undersampling depends on the gap between them.

## Slide 42
Analog input bandwidth
Part 5 · Bandwidth and sampling
42
BW₋₃dB · Hz
How high in frequency the sample-and-hold front end will still faithfully follow the input, measured where the response has fallen 3 dB. It is completely independent of the sample rate, and it is often several times higher.
BW₋₃dB = 1 / (2π τ)
Set by the input switch resistance and hold capacitance
Chart: frequency (MHz) · −3 dB at 900 MHz, far above Nyquist
| 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 4 | 4 | 5 | 6 | 7 | 7 | 8 | 9 | 11 | 12 | 14 | 16 | 18 | 20 | 23 | 26 | 29 | 33 | 37 | 42 | 48 | 54 | 62 | 70 | 79 | 90 | 102 | 115 | 130 | 148 | 167 | 190 | 215 | 243 | 276 | 313 | 354 | 401 | 455 | 515 | 584 | 661 | 749 | 849 | 962 | 1090 | 1235 | 1399 | 1585
input response (dB) | -5.3617e-06 | -6.8829e-06 | -8.8358e-06 | -1.1343e-05 | -1.4561e-05 | -1.8693e-05 | -2.3996e-05 | -3.0805e-05 | -3.9545e-05 | -5.0765e-05 | -6.5169e-05 | -8.366e-05 | -0.0001074 | -0.00013787 | -0.00017698 | -0.0002272 | -0.00029166 | -0.00037441 | -0.00048064 | -0.000617 | -0.00079205 | -0.0010168 | -0.0013052 | -0.0016754 | -0.0021507 | -0.0027607 | -0.0035437 | -0.0045487 | -0.0058384 | -0.0074935 | -0.0096174 | -0.012342 | -0.015838 | -0.020321 | -0.026069 | -0.033438 | -0.042878 | -0.054968 | -0.070438 | -0.090217 | -0.11548 | -0.14769 | -0.1887 | -0.24078 | -0.30673 | -0.38995 | -0.4945 | -0.62513 | -0.78727 | -0.9869 | -1.2304 | -1.5243 | -1.8745 | -2.2863 | -2.7635 | -3.3079 | -3.9197 | -4.5966 | -5.3348 | -6.129
Nyquist, 125 MHz | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60 | -60
A wide input bandwidth also lets in wideband noise and out-of-band interference, so the anti-alias filter has to do more work, not less.
≈
Think of it like this How high a note a microphone can pick up, which is a different question from how many times a second you write the level down.
EXAMPLE
A typical high-speed part
Sample rate 250 MSPS, so Nyquist is 125 MHz
Analog bandwidth 900 MHz — more than seven times higher
That headroom is what makes undersampling a 400 MHz IF possible
Notes: Definition: How high in frequency the sample-and-hold front end will still faithfully follow the input, measured where the response has fallen 3 dB. It is completely independent of the sample rate, and it is often several times higher. Analogy: How high a note a microphone can pick up, which is a different question from how many times a second you write the level down. Example (A typical high-speed part): Sample rate 250 MSPS, so Nyquist is 125 MHz; Analog bandwidth 900 MHz — more than seven times higher; That headroom is what makes undersampling a 400 MHz IF possible. Why it matters: A wide input bandwidth also lets in wideband noise and out-of-band interference, so the anti-alias filter has to do more work, not less.

## Slide 43
Full-power and full-linear bandwidth
Part 5 · Bandwidth and sampling
43
FPBW, FLBW · Hz
Two more honest bandwidth numbers. Full-power bandwidth is where a full-scale input has dropped 3 dB. Full-linear bandwidth is the much lower frequency up to which the converter still meets its distortion specification — and that is the one you can actually use.
FLBW < FPBW < BW_small-signal
Almost always in that order
Chart: three bandwidths for one converter
| small signal −3 dB | full power −3 dB | full linear (SFDR > 70 dB)
MHz | 900 | 500 | 200
Never design to the headline bandwidth. Find the frequency at which ENOB and SFDR are still adequate, and treat that as the real limit.
≈
Think of it like this A car’s top speed against the speed at which it still handles safely. The brochure quotes one; you drive at the other.
EXAMPLE
The gap is large
Small-signal bandwidth: 900 MHz
Full-power bandwidth: 500 MHz
Full-linear bandwidth (SFDR still above 70 dB): 200 MHz
Notes: Definition: Two more honest bandwidth numbers. Full-power bandwidth is where a full-scale input has dropped 3 dB. Full-linear bandwidth is the much lower frequency up to which the converter still meets its distortion specification — and that is the one you can actually use. Analogy: A car’s top speed against the speed at which it still handles safely. The brochure quotes one; you drive at the other. Example (The gap is large): Small-signal bandwidth: 900 MHz; Full-power bandwidth: 500 MHz; Full-linear bandwidth (SFDR still above 70 dB): 200 MHz. Why it matters: Never design to the headline bandwidth. Find the frequency at which ENOB and SFDR are still adequate, and treat that as the real limit.

## Slide 44
Undersampling and bandpass sampling
Part 5 · Bandwidth and sampling
44
Aliasing used deliberately. A signal in a narrow band high up in frequency can be sampled far below its own frequency: it folds down into the first Nyquist zone intact, with the ADC doing the work of a mixer.
2 f_H / n ≤ f_s ≤ 2 f_L / (n − 1)
Keeps the band [f_L, f_H] clear of the fold points
requires BW_analog > f_H
The front end must genuinely reach the real frequency
Chart: a 70 MHz IF lives in zone 3 and folds down into zone 1
| zone 1 | zone 2 | zone 3 | zone 4 | zone 5 | zone 6
upper edge (MHz), f_s = 61.44 MSPS | 30.72 | 61.44 | 92.16 | 122.88 | 153.6 | 184.32
The jitter penalty is set by the real input frequency, not the sample rate. Undersampling a high IF is the hardest thing you can ask of a sampling clock.
≈
Think of it like this Watching a fast fan under a strobe light tuned so the blades appear to creep slowly. Nothing about the fan changed; you chose a look rate that makes it easy to watch.
EXAMPLE
A 70 MHz IF at 61.44 MSPS
The band 65 – 75 MHz folds into the second Nyquist zone
It folds down to |70 − 61.44| = 8.56 MHz, orientation intact (zone 3 is odd)
Needs a sharp bandpass filter and very low jitter, because 70 MHz sets the jitter budget
Notes: Definition: Aliasing used deliberately. A signal in a narrow band high up in frequency can be sampled far below its own frequency: it folds down into the first Nyquist zone intact, with the ADC doing the work of a mixer. Analogy: Watching a fast fan under a strobe light tuned so the blades appear to creep slowly. Nothing about the fan changed; you chose a look rate that makes it easy to watch. Example (A 70 MHz IF at 61.44 MSPS): The band 65 – 75 MHz folds into the second Nyquist zone; It folds down to |70 − 61.44| = 8.56 MHz, orientation intact (zone 3 is odd); Needs a sharp bandpass filter and very low jitter, because 70 MHz sets the jitter budget. Why it matters: The jitter penalty is set by the real input frequency, not the sample rate. Undersampling a high IF is the hardest thing you can ask of a sampling clock.

## Slide 45
Oversampling ratio and decimation
Part 5 · Bandwidth and sampling
45
OSR · ×
Sampling much faster than Nyquist spreads the same fixed quantisation noise over a wider band. A digital filter then keeps only the band you care about and throws the rest away — taking most of the noise with it.
OSR = f_s / (2 × BW)
How many times faster than strictly necessary
gain = 10 log₁₀(OSR)
+3 dB per doubling, plain oversampling
Chart: oversampling ratio
| 1 | 4 | 16 | 64 | 256 | 1024
plain | 0 | 6.0206 | 12.0412 | 18.0618 | 24.0824 | 30.103
1st order | 0 | 18 | 36 | 54 | 72 | 90
2nd order | 0 | 30 | 60 | 90 | 120 | 150
This is the whole trick behind delta-sigma converters, and it is why they can be extremely accurate and quite slow at the same time.
≈
Think of it like this Weighing a letter on a coarse scale a thousand times while nudging it, then averaging. Many rough measurements, carefully combined, beat one careful measurement.
EXAMPLE
A 24-bit audio converter
1-bit modulator at 6.1 MSPS, signal band 20 kHz → OSR = 153
Seven doublings with second-order shaping: 7 × 15 = 105 dB gained
A one-bit front end ends up delivering about 20 real bits
Notes: Definition: Sampling much faster than Nyquist spreads the same fixed quantisation noise over a wider band. A digital filter then keeps only the band you care about and throws the rest away — taking most of the noise with it. Analogy: Weighing a letter on a coarse scale a thousand times while nudging it, then averaging. Many rough measurements, carefully combined, beat one careful measurement. Example (A 24-bit audio converter): 1-bit modulator at 6.1 MSPS, signal band 20 kHz → OSR = 153; Seven doublings with second-order shaping: 7 × 15 = 105 dB gained; A one-bit front end ends up delivering about 20 real bits. Why it matters: This is the whole trick behind delta-sigma converters, and it is why they can be extremely accurate and quite slow at the same time.

## Slide 46
Part 6
Power, interface and figures of merit
What it costs, how you get the data out, and how to compare parts fairly
8 minutes
46
Notes: The commercial half of the datasheet.

## Slide 47
Power dissipation and supplies
Part 6 · Power, interface and figures of merit
47
P_D · W
What the converter costs you in watts, usually split across an analogue supply, a digital supply and an I/O supply. It scales roughly with sample rate, and very steeply with resolution — every extra bit costs about four times the power.
P ∝ f_s × 2²ᴺᵒᵇ
Why 16 bits at 1 GSPS is so much harder than 8 bits at 1 GSPS
Chart: roughly 4× per extra bit
| 8 bit | 10 bit | 12 bit | 14 bit | 16 bit
power at 100 MSPS (mW) | 20 | 80 | 320 | 1280 | 5120
In battery and multi-channel systems, energy per conversion matters more than the headline power figure — which is exactly what the next two slides…
≈
Think of it like this Precision costs energy everywhere: a laboratory balance uses far more power than a kitchen scale, for the same reason.
EXAMPLE
Comparing two parts
12 bit, 100 MSPS: 300 mW → 3 nJ per conversion
16 bit, 100 MSPS: 1.4 W → 14 nJ per conversion
Many parts offer a low-power mode that trades sample rate for milliwatts
Notes: Definition: What the converter costs you in watts, usually split across an analogue supply, a digital supply and an I/O supply. It scales roughly with sample rate, and very steeply with resolution — every extra bit costs about four times the power. Analogy: Precision costs energy everywhere: a laboratory balance uses far more power than a kitchen scale, for the same reason. Example (Comparing two parts): 12 bit, 100 MSPS: 300 mW → 3 nJ per conversion; 16 bit, 100 MSPS: 1.4 W → 14 nJ per conversion; Many parts offer a low-power mode that trades sample rate for milliwatts. Why it matters: In battery and multi-channel systems, energy per conversion matters more than the headline power figure — which is exactly what the next two slides measure.

## Slide 48
Walden figure of merit
Part 6 · Power, interface and figures of merit
48
FoM_W · J/conversion-step
Energy spent for each conversion, divided by the number of levels actually resolved. It lets you compare a slow precision part against a fast coarse one on equal terms. Lower is better.
FoM_W = P / ( 2^ENOB × f_s )
Joules per conversion step
Chart: lower is better
| 8b 1 GSPS | 12b 100 MSPS | 16b 10 MSPS | 24b 1 kSPS
pJ per conversion step | 2.7621 | 1.0358 | 0.5179 | 0.95367
≈
Think of it like this Litres per hundred kilometres for cars. It lets you compare a small hatchback with a lorry, because it divides out how much work each is doing.
EXAMPLE
Is 300 mW good?
12 bit, ENOB 11.5, 100 MSPS, 300 mW
FoM = 0.3 / (2^11.5 × 1e8) = 1.04 pJ per step
State of the art is a few femtojoules; 1 pJ is respectable for a fast part
Notes: Definition: Energy spent for each conversion, divided by the number of levels actually resolved. It lets you compare a slow precision part against a fast coarse one on equal terms. Lower is better. Analogy: Litres per hundred kilometres for cars. It lets you compare a small hatchback with a lorry, because it divides out how much work each is doing. Example (Is 300 mW good?): 12 bit, ENOB 11.5, 100 MSPS, 300 mW; FoM = 0.3 / (2^11.5 × 1e8) = 1.04 pJ per step; State of the art is a few femtojoules; 1 pJ is respectable for a fast part. For the experts: Walden implicitly assumes power scales with 2^ENOB, which holds while the design is limited by comparator and switching energy. Once thermal noise dominates, power scales with 2^(2·ENOB) and the Schreier figure is the fairer comparison.

## Slide 49
Schreier figure of merit
Part 6 · Power, interface and figures of merit
49
FoM_S · dB
The other way of asking the same question, built for converters whose limit is thermal noise rather than switching energy. Higher is better, and it is the figure used for precision and delta-sigma parts.
FoM_S = SNDR + 10 log₁₀( BW / P )
dB; add 10 log₁₀ of bandwidth per watt
Chart: higher is better
| 8b 1 GSPS | 12b 100 MSPS | 16b 10 MSPS | 24b 1 kSPS
FoM_S (dB) | 135 | 152.7185 | 164.1979 | 173.9794
Use Walden for fast, low-resolution parts and Schreier for slow, high-resolution ones. Quoting the wrong one flatters the wrong design.
≈
Think of it like this Rating a telescope by how faint a star it can see per unit of cost. It rewards sensitivity, not just size.
EXAMPLE
The same part
SNDR 70.5 dB, bandwidth 50 MHz, power 300 mW
FoM_S = 70.5 + 10 log₁₀(5e7 / 0.3) = 152.7 dB
Above about 175 dB is state of the art
Notes: Definition: The other way of asking the same question, built for converters whose limit is thermal noise rather than switching energy. Higher is better, and it is the figure used for precision and delta-sigma parts. Analogy: Rating a telescope by how faint a star it can see per unit of cost. It rewards sensitivity, not just size. Example (The same part): SNDR 70.5 dB, bandwidth 50 MHz, power 300 mW; FoM_S = 70.5 + 10 log₁₀(5e7 / 0.3) = 152.7 dB; Above about 175 dB is state of the art. Why it matters: Use Walden for fast, low-resolution parts and Schreier for slow, high-resolution ones. Quoting the wrong one flatters the wrong design.

## Slide 50
Crosstalk and channel isolation
Part 6 · Power, interface and figures of merit
50
In a multi-channel converter, how much of a signal on one channel leaks into another. A large signal on channel 1 can put a ghost of itself on channel 2, where nothing was connected at all.
crosstalk = 20 log₁₀( V_leaked / V_source )
More negative is better; worsens with frequency
Chart: frequency (Hz) · isolation always worsens with frequency
| 10 | 100 | 1 k | 10 k | 100 k
crosstalk (dB) | -110 | -100 | -90 | -80 | -70
Multiplexed converters also suffer settling crosstalk: the previous channel’s voltage has not fully decayed from the hold capacitor when the next is…
≈
Think of it like this Hearing next door’s television faintly through the wall. Nothing is wrong with your television; the isolation between rooms is finite.
EXAMPLE
An 8-channel data logger
Channel 1: 10 V thermocouple amplifier output
Crosstalk −80 dB → 1 mV appears on channel 2
On a 16-bit, 2 V range that is 33 LSB of pure fiction
Notes: Definition: In a multi-channel converter, how much of a signal on one channel leaks into another. A large signal on channel 1 can put a ghost of itself on channel 2, where nothing was connected at all. Analogy: Hearing next door’s television faintly through the wall. Nothing is wrong with your television; the isolation between rooms is finite. Example (An 8-channel data logger): Channel 1: 10 V thermocouple amplifier output; Crosstalk −80 dB → 1 mV appears on channel 2; On a 16-bit, 2 V range that is 33 LSB of pure fiction. Why it matters: Multiplexed converters also suffer settling crosstalk: the previous channel’s voltage has not fully decayed from the hold capacitor when the next is sampled.

## Slide 51
Digital interface
Part 6 · Power, interface and figures of merit
51
How the numbers leave the chip. The choice is set by the data rate: a slow part can use a handful of wires and a simple protocol, while a gigasample part needs serialised high-speed lanes.
SPI or I²C: a few hundred kSPS to a few MSPS, simplest wiring
Parallel CMOS: fast but many pins, and the switching noise couples back into the analogue
LVDS: differential, low noise, good to hundreds of MSPS
JESD204B/C: serialised lanes with deterministic latency, for GSPS parts and synchronised arrays
Interface | Typical rate | Where it fits
SPI / I²C | < 50 Mbit/s | Sensors, slow SAR
Parallel CMOS | < 1 Gbit/s | Mid-speed, many pins
LVDS | ~ 1 Gbit/s per pair | 100s of MSPS
JESD204B/C | 12.5 Gbit/s per lane | GSPS, synchronised arrays
Digital switching noise coupling back into the analogue front end is a real and common problem. It is one of the reasons LVDS and serialised interfaces…
≈
Think of it like this The difference between handing over a note, posting a letter, and running a dedicated fibre. All deliver the message; they differ in how much you can send and how much fuss it is.
EXAMPLE
Sizing the link
12 bit at 250 MSPS = 3 Gbit/s of payload
Too fast for parallel CMOS at sensible pin counts
Two JESD204B lanes at 5 Gbit/s each, with 8b/10b overhead, carry it comfortably
Notes: Definition: How the numbers leave the chip. The choice is set by the data rate: a slow part can use a handful of wires and a simple protocol, while a gigasample part needs serialised high-speed lanes. Analogy: The difference between handing over a note, posting a letter, and running a dedicated fibre. All deliver the message; they differ in how much you can send and how much fuss it is. Example (Sizing the link): 12 bit at 250 MSPS = 3 Gbit/s of payload; Too fast for parallel CMOS at sensible pin counts; Two JESD204B lanes at 5 Gbit/s each, with 8b/10b overhead, carry it comfortably. Why it matters: Digital switching noise coupling back into the analogue front end is a real and common problem. It is one of the reasons LVDS and serialised interfaces won.

## Slide 52
Part 7
Architectures and the datasheet
Which converter, and how to read its datasheet in the right order
12 minutes
52
Notes: Bringing all the parameters together into a choice.

## Slide 53
The five architectures compared
Part 7 · Architectures and the datasheet
53
Every architecture is a different way of doing the quantise step, and each one trades the parameters in this talk against each other differently.
Architecture | Speed | Resolution | Latency | Strength | Weakness
Flash | GSPS | 4 – 8 bit | 1 cycle | Fastest possible; one clock per result | 2ᴺ−1 comparators: power and area explode
SAR | kSPS – 100s MSPS | 8 – 18 bit | N cycles, no pipeline | Excellent power efficiency; zero latency | One result per N clocks
Pipeline | 10s MSPS – GSPS | 10 – 16 bit | 8 – 16 cycles | Best speed-resolution product | Latency; needs calibration
Delta-sigma | kSPS – 10s MSPS | 16 – 24 bit | Long (filter) | Superb DNL and dynamic range | Slow; heavy digital filtering
Dual-slope | Hz – kSPS | 12 – 22 bit | Very long | Rejects mains hum inherently; very linear | Far too slow for signals
No architecture wins everywhere. Choosing one is choosing which parameter you are willing to give up.
Notes: Walk the table column by column. The point is that no architecture wins everywhere: the choice is which parameter you are willing to give up. Definition: Every architecture is a different way of doing the quantise step, and each one trades the parameters in this talk against each other differently.

## Slide 54
Reading a datasheet in the right order
Part 7 · Architectures and the datasheet
54
Datasheets are written to flatter. Reading them in this order stops you being flattered.
1
Sample rate and analog bandwidth Can it reach your input frequency at all? Bandwidth must exceed the real input frequency, not just Nyquist.
2
ENOB at your input frequency Find the ENOB-versus-frequency curve. The headline resolution is the marketing number; this is the engineering one.
3
SFDR at your input frequency If a strong signal will sit near a weak one, this decides whether you can see the weak one.
4
The jitter budget Compute 1/(2π f_in × 10^(SNR/20)). If it is under a picosecond, your clock is now a major design problem.
5
Driver and settling requirements Track time divided by ln(2^(N+1)) gives the time constant your amplifier must achieve.
6
Static specs, only if you measure DC For AC work, offset and gain are irrelevant; INL still matters because it sets distortion.
7
Power, latency and interface The constraints that decide whether the part fits the product rather than the signal.
Notes: This is the practical takeaway slide. Encourage people to photograph it. Definition: Datasheets are written to flatter. Reading them in this order stops you being flattered.

## Slide 55
Worked example: choosing a converter
Part 7 · Architectures and the datasheet
55
A 20 MHz-wide radio channel at a 70 MHz intermediate frequency, needing 60 dB of usable dynamic range in a battery-powered product.
Sample rate: 20 MHz band → at least 44 MSPS; pick 61.44 MSPS and undersample the 70 MHz IF
Analog bandwidth: must exceed 70 MHz comfortably — look for 300 MHz or more
Resolution: 60 dB needed + 12 dB headroom + margin → 12 bits (74 dB ideal)
ENOB at 70 MHz: must still be above 10.5 — check the curve, not the headline
Jitter: 12 bits at 70 MHz needs about 450 fs total, clock included
SFDR: at least 75 dB, because a strong neighbouring channel is guaranteed
Requirement | Value
Signal band | 20 MHz at a 70 MHz IF
Sample rate | 61.44 MSPS (undersampling zone 3)
Analog bandwidth | > 300 MHz
Resolution | 12 bit (74 dB ideal)
ENOB at 70 MHz | > 10.5 bits
Jitter budget | 455 fs total
SFDR | > 75 dBc
Notice that resolution was decided fourth, not first. The frequency-dependent parameters did most of the work.
≈
Think of it like this Specifying a car by the journey rather than the brochure: how far, how fast, how much luggage, how much fuel.
EXAMPLE
The numbers that decide it
Jitter budget: 1/(2π × 70e6 × 10^(74/20)) = 455 fs
FFT floor with a 4096-point transform: −74 − 33 = −107 dBFS
Power target under 200 mW → FoM_W must beat about 0.7 pJ per step
Notes: Definition: A 20 MHz-wide radio channel at a 70 MHz intermediate frequency, needing 60 dB of usable dynamic range in a battery-powered product. Analogy: Specifying a car by the journey rather than the brochure: how far, how fast, how much luggage, how much fuel. Example (The numbers that decide it): Jitter budget: 1/(2π × 70e6 × 10^(74/20)) = 455 fs; FFT floor with a 4096-point transform: −74 − 33 = −107 dBFS; Power target under 200 mW → FoM_W must beat about 0.7 pJ per step. Why it matters: Notice that resolution was decided fourth, not first. The frequency-dependent parameters did most of the work.

## Slide 56
Seven ways these parameters catch people out
Part 7 · Architectures and the datasheet
56
1
Trusting resolution
A "16-bit" part delivering 12.5 ENOB at your frequency is a 12.5-bit part. Always read ENOB at the input frequency you will actually use.
2
Comparing noise floors
Two FFT plots with different lengths are not comparable. Subtract 10 log₁₀(N/2) before you believe either of them.
3
Ignoring the driver
Under-settling in the amplifier in front of the ADC appears in the FFT as distortion. The converter gets blamed for the driver’s sins.
4
Jitter follows f_in
Undersampling a 200 MHz IF at 50 MSPS needs the jitter budget for 200 MHz, not 50 MHz. This surprises people constantly.
5
Calibrating once
Room-temperature calibration removes offset and gain, and nothing at all of the drift that follows.
6
THD with two signals
Single-tone distortion can look excellent while two-tone IMD is poor. Receivers must be specified on IMD.
7
No headroom
Running close to full scale to "use all the bits" means the first signal peak clips and fills the spectrum with harmonics.
Notes: Each of these is a real, recurring failure. Invite the room to add their own.

## Slide 57
Every parameter on one slide
Resolution | levels = 2ᴺ; LSB = FSR / 2ᴺ
Quantisation | −½ ≤ e_q < +½ LSB; noise power = LSB²/12
Offset / gain | shift of the staircase / wrong slope; both calibratable
DNL | step width / LSB − 1; ≤ −1 LSB means a missing code
INL | Σ DNL; sets the distortion floor, so it caps SFDR
TUE | √(E_O² + E_G² + INL² + …) for an uncalibrated system
SNR | 6.02 N + 1.76 dB ideal; harmonics excluded
THD | 10 log₁₀(ΣP_harmonics / P_signal), in dBc
SINAD | signal over noise + distortion together
ENOB | (SINAD − 1.76 + back-off) / 6.02
SFDR | signal over the largest single spur, harmonic or not
FFT floor | −SNR − 10 log₁₀(N/2), so it moves with transform length
Jitter | SNR = −20 log₁₀(2π f_in t_j); uses input frequency
Settling | ln(2^(N+1)) time constants to reach ½ LSB
Slew needed | π × FSR × f for a full-scale sine
Oversampling | +10 log₁₀(OSR); (6L+3) dB per doubling with L-th order shaping
Walden FoM | P / (2^ENOB × f_s); lower is better
Schreier FoM | SNDR + 10 log₁₀(BW / P); higher is better
57
Notes: The photograph slide. Leave it up during questions.

## Slide 58
Questions?
Further reading
W. Kester (ed.), The Data Conversion Handbook, Analog Devices — the definitive reference
W. Kester, "Understand SINAD, ENOB, SNR, THD, THD + N, and SFDR", Analog Devices MT-003
IEEE Std 1241, Terminology and Test Methods for Analog-to-Digital Converters
R. van de Plassche, CMOS Integrated Analog-to-Digital and Digital-to-Analog Converters
B. Murmann, "ADC Performance Survey" — the running database behind both figures of merit
58
Notes: No notes.